## Slide 1: New England Nuclear: Present and Future
Armond Cohen, Executive Director
Clean Air Task Force

## Slide 2
Rockstrom, et al (2017)

## Slide 3: Every molecule matters today
Half life of CO2 in atmosphere is 500-1000 years
It’s the cumulative CO2 that matters
So, whatever you think the energy mix will or should look like in 2050, the transition matters
Keeping every existing zero carbon source online where possible during the transition is important

## Slide 4: So where does nuclear fit in?
A “today” tool to suppress CO2 accumulation – should be maintained and built upon
Possibly part of a zero carbon 2050 + end-state, but better cost performance will likely be required (at least in the US)

## Slide 5: Why not bet on all renewables?
Scaling rates, especially important during transition
Management of multi-day, weekly and SEASONAL surplus and deficit at high penetration Higher cost

## Slide 6
Chart: New England Demand vs Zero Carbon Resources (GWh)
| Total NE load 2016 | Millstone and Seabrook 2016 | Wind and solar
Wind 2016 | 124258 | 27085 | 2519
Solar 2026 | 8292
50% of wind in queue | 7000
MA offshore wind 1600 MW | 7008

## Slide 7: Monthly capacity factor for New England terrestrial wind
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 0.39 | 0.36 | 0.38 | 0.36 | 0.25 | 0.22 | 0.21 | 0.17 | 0.26 | 0.34 | 0.41 | 0.3

## Slide 8
Chart: MONTHLY CAPACITY FACTOR DEEP OFFSHORE NORTHEAST WIND SITE LAT -70.4301, LONG 38.47374 NREL WIND DATABASE ANNUAL CAPACITY FACTOR = 49.8%
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
 | 0.7631 | 0.64179 | 0.5323 | 0.56641 | 0.46104 | 0.41311 | 0.31192 | 0.25784 | 0.28793 | 0.39868 | 0.71505 | 0.62511

## Slide 9
Chart: MONTHLY CAPACITY FACTOR SOLAR NREL INSOLATION DATA FOR BOSTON
PV | 0.09879 | 0.13318 | 0.1586 | 0.17361 | 0.19086 | 0.19375 | 0.1959 | 0.18716 | 0.15591 | 0.13844 | 0.092361 | 0.084341

## Slide 10
Chart: ISO NE SCENARIOS MAY – ABUNDANT SURPLUS RPS 80

## Slide 11
Chart: ISO NE SCENARIOS DECEMBER – LITTLE SURPLUS RPS 80

## Slide 12: This assumes 383,241 MWH STORAGE
55 million Tesla Powerwall batteries
  $165 billion (at $3000 each installed or < half of current cost)
  Four per capita
  763 per square mile
46 new Northfield Mountain facilities

## Slide 13
Chart: ISO NE SCENARIOS DECEMBER – LITTLE SURPLUS RPS 80
DR = 3500 MW

## Slide 15: But for nuclear to play, US costs must come down
Chart: Unit costs ($/kw)
| AP-1000- Georgia (estimated before latest Westinghouse bankruptcy) | UAE KEPCO delivered contract price
 | 7740 | 3570

## Slide 16: How?
Use of different coolants that remain stable at higher temperature ranges (e.g. molten salts, sodium, helium) and can operate at atmospheric pressure
This reduces need for pressurized containment (as much as two thirds of plant steel and concrete)
This enables a factory/manufacturing model faster, more predictable completion times
Recent survey: all-in LCOE at $40-60 MWH is attainable

## Slide 18: Who?

## Slide 19: When?
Many US and Canadian developers looking to first commercial plant at or before 2030.
China HTGR online 2018

## Slide 20: Summary
The climate lift is big, and will require a near-zero carbon grid
Existing New England nuclear significantly suppresses CO2 accumulation, and will be hard to replace quickly.
An 80-100% wind and solar grid faces significant costly seasonal balancing issues
Recommendations:
  Preserve existing New England nuclear, at least for the transition
  Make space for new nuclear to compete in low carbon preference policies – as in proposed Massachusetts Clean Energy Standard

## Slide 21: Extra slides